## Slide 1: Real-Time BLDC Motor Condition Monitoring, Fault Detection and Predictive Maintenance Using ESP32
PROJECT PRESENTATION · GROUP 17
MUKUNDAN · CB.EN.U4EEE24124
SADA SIVA SURYA SRINIVAS · CB.EN.U4EEE24128
Department of EEE | Amrita Vishwa Vidyapeetham
Notes: Introduce Group 17, the two team members and the project title.

## Slide 2: Current Problem
≈ 70%
of industrial electrical energy is consumed by motors
Conventional BLDC drives only control speed and torque.
Unexpected motor failure
High maintenance cost
Production downtime
Energy wastage
Manual inspection
No remote monitoring
Modern industries need intelligent drives with health monitoring and predictive maintenance.
Notes: Industrial motors use most of the electrical energy, and unexpected failures cause downtime. Conventional BLDC drives only control speed and torque.

## Slide 3: Literature Review
1
Raja et al. (2022)
Cost-efficient real-time condition monitoring and fault diagnostics system for BLDC motor using IoT and machine learning
BLDC · IoT + ML
2
IoT based condition monitoring (2022)
IoT based condition monitoring and control of induction motor using Raspberry Pi
Induction · Raspberry Pi
3
do Nascimento, da Silva & Pereira (2024)
Development of a data acquisition and monitoring system for electric motors using the Internet of Things
ESP32 · temp, current, vibration
4
Arman Sabri & Aziz (2025)
Motor vibration and temperature detector by using IoT
ESP32 · DS18B20 · Blynk
5
Wan Mohd Supian et al. (2022)
Electrical machine breakdown monitoring system using IoT
ESP32 · ACS712 · Blynk
Most reviewed work targets induction or AC motors and monitors only a few parameters.
Notes: Five related studies. Four monitor induction or AC motors with ESP32 or Raspberry Pi platforms; only one targets BLDC motors.

## Slide 4: Research Gap
Existing systems
BLDC drives only perform speed control
Monitoring tracks temperature, current or vibration alone
Expensive
Separate hardware required
Research gap
No low-cost integrated BLDC drive combining:
Power electronics
Drive control
Energy monitoring
IoT
Predictive maintenance
Notes: Existing drives only control speed and existing monitors cover single parameters; no low-cost integrated BLDC drive combines the five capabilities.

## Slide 5: Novelty
WHAT IS NEW
The system turns a conventional BLDC drive into an intelligent, self-monitoring drive on a single low-cost platform. Unlike systems that only control the motor or watch isolated parameters, it continuously evaluates motor health and gives early maintenance recommendations while keeping operation efficient.
Power electronics
Motor protection
Multi-parameter monitoring
IoT remote supervision
Energy analytics
Predictive maintenance
Notes: One low-cost platform that combines drive, monitoring, IoT and predictive maintenance.

## Slide 6: Objectives
1
Design and simulate a BLDC motor drive with a three-phase power converter
2
Protect the motor by disabling the drive on critical faults
3
Monitor voltage, current, power and energy in real time
4
Monitor motor vibration and temperature
5
Detect overload, overheating and mechanical abnormalities by multi-parameter analysis
6
Enable IoT remote monitoring with ESP32 and a cloud dashboard
7
Provide predictive maintenance with early fault warnings
8
Validate through MATLAB/Simulink simulation and hardware implementation
Notes: Eight objectives covering the drive, monitoring, fault detection, IoT, predictive maintenance and validation.

## Slide 7: Methodology
1
Literature Survey
BLDC drives, fault detection, IoT monitoring, predictive maintenance
2
BLDC Drive Modeling
Simulink: DC source, three-phase converter, commutation, BLDC motor
3
Drive Control
Fixed commutation, no speed loop
4
Parameter Monitoring
Voltage, current, power, energy, temperature, vibration
5
Fault Simulation
Overload, over-temperature and mechanical vibration faults
6
Fault Detection
Classify condition: Healthy, Warning or Fault
7
Predictive Maintenance
Estimate motor health from sensor data and raise maintenance alerts
8
IoT Integration
ESP32 sends live data to a cloud dashboard
9
Validation
Compare MATLAB simulation with hardware results
Notes: Nine steps from literature survey to validation.

## Slide 8: Proposed Solution
1 DRIVE
2 MONITOR
3 ACT & SHARE
24 V DC source
Three-phase inverter
fixed commutation, no speed loop
BLDC motor + load
Voltage
Current
Temperature
Vibration
ESP32
power & energy · fault detection · health score
OLED display
12 live pages
Blynk dashboard
remote monitoring
Protection trip
EN pin disables the driver
The speed is not controlled: the drive runs on fixed commutation while the ESP32 monitors and protects it.
Notes: Three stages: the drive runs on fixed commutation with no speed control; sensors and the ESP32 monitor it; results go to the OLED and Blynk and a protection trip can disable the driver.

## Slide 9: Simulation Base Model
Notes: MATLAB/Simulink model: DC source, converter, BLDC motor, commutation logic, load and four fault-monitoring subsystems (current, voltage, vibration, temperature) with lamps and status displays.

## Slide 10: Simulation Circuit Diagram
Gate drive: Ga, Gb, Gc (H / L)
+24 V
0 V
24 V
DC
V
A
Ga(H)
+ diode
Ga(L)
+ diode
Gb(H)
+ diode
Gb(L)
+ diode
Gc(H)
+ diode
Gc(L)
+ diode
BLDC
Motor
A
B
C
Load
(J, T)
Motor thermal ports and rotor speed feed the temperature and vibration subsystems.
Commutation logic (MATLAB function)
fixed duty 0.3 · carrier · 2 pole pairs · no speed loop
Hall HA, HB, HC (rotor position)
A Current sensor
V Voltage sensor
Notes: Power circuit of the Simulink model: 24 V DC source, current and voltage sensors, a three-phase six-switch converter driven by the commutation logic with fixed duty 0.3, and the BLDC motor with its load. There is no speed controller.

## Slide 11: Commutation & Power Stage
Commutation Logic
Uses rotor position feedback to generate the gate-switching sequence for electronic commutation.
Three-Phase Power Converter
Switches chop the 24 V DC input into regulated three-phase PWM voltages for the motor phases.
BLDC Motor Block
Simscape model that converts electrical energy into mechanical rotation and torque.
Sector table
Sector | High side (PWM) | Low side (on) | Floating
0 | A | B | C
1 | A | C | B
2 | B | C | A
3 | B | A | C
4 | C | A | B
5 | C | B | A
Notes: Commutation uses rotor position to pick which phases are driven; the converter chops the 24 V supply into three-phase PWM voltages.

## Slide 12: Gating Signals
High side
Switched with PWM chopping
Low side
Held ON during its sector
Sector
Chosen from rotor position
Notes: Six gate signals: Ga, Gb and Gc, each with a high-side (H) and a low-side (L) signal.

## Slide 13: Phase Voltage & Current Waveforms
Top: phase A voltage · Bottom: phase A current
1
Low side ON
0 V · current negative, growing
2
Low side turns off
Spike to 24 V · current falls to 0
3
Phase open
Voltage follows back-EMF · current 0
4
High side PWM
Dense 24 V pulses · current rises
5
Both OFF
Flat −1 V · current decays slowly
6
Low side ON again
Back to 0 V · cycle repeats
Notes: Phase A voltage (top) and current (bottom) over one electrical cycle, split into six stages.

## Slide 14: Phase A: Gating vs Response
Ga(H) bursts
PWM bursts produce the voltage pulses
Ga(L) pulses
0 V and negative current while the low side conducts
Every cycle
Current repeats with the commutation pattern
Notes: Ga(H) and Ga(L) gate signals with the resulting phase A voltage and current.

## Slide 15: Load & Vibration Subsystems
Load subsystem
Generates the mechanical resistance the motor works against. It takes rotor speed, adds drag and step loads in a Sum block, and drives the Ideal Torque Source to brake the shaft.
Vibration subsystem
Rotor position goes through a sine block and gain 0.05 into the load Sum block to inject ripple. Detection: filtered speed difference, low-pass filter, compare > 2.
Notes: Load subsystem creates the opposing torque; the vibration subsystem injects ripple and detects it.

## Slide 16: Current & Voltage Subsystems
Current subsystem
Phase current is low-pass filtered to strip PWM noise, compared with 0.9 A and gated by a step enable to raise the fault flag.
Voltage subsystem
A voltage sensor across the DC link feeds a compare-to-constant (> 24) block that sets the over-voltage flag.
Notes: Current is filtered and compared with 0.9 A; DC-link voltage is compared with 24 V.

## Slide 17: Temperature Subsystem
Thermal path
BLDC thermal ports (HA, HB, HC, HR) connect through a 2 K/W thermal resistance to a 30 °C ambient source.
Detection
Sensor output in kelvin minus 273.15 gives °C; a compare block flags a fault above 70 °C.
Notes: Thermal ports of the BLDC model connect through a 2 K/W thermal resistance to a 30 degC ambient source; the sensed temperature is compared with 70 degC.

## Slide 18: Current Output
Condition: A fault is triggered whenever the motor current exceeds 0.9 A.
NORMAL
Top: fault flag · Bottom: current
Steady state: the motor draws 0.5068 A against a load torque of −0.01841 N·m.
FAULT
Top: fault flag · Bottom: current
Current surges to 1.357 A against an opposing torque of −0.1554 N·m; the flag goes high.
Notes: Normal vs fault current waveforms with the fault indicator.

## Slide 19: Voltage Output
Condition: An over-voltage is detected whenever the supply voltage rises above 24 V.
NORMAL
Top: supply voltage · Bottom: fault flag
Stable input and output voltage of 24 V; no fault.
FAULT
Top: supply voltage · Bottom: fault flag
Supply raised to the fault level of 30 V; the over-voltage flag is set.
Notes: Supply voltage and fault flag for normal and over-voltage cases.

## Slide 20: Vibration Output
Condition: A high-vibration fault is registered whenever the output exceeds 2.
NORMAL
Top: vibration · Bottom: fault flag
Vibration level of 0.5147 with zero torque ripple.
FAULT
Top: vibration · Bottom: fault flag
With the ripple circuit active the output reaches 3.459 (torque ripple 0.002688); the flag is set.
Notes: Vibration level and fault flag.

## Slide 21: Temperature Output
Condition: A thermal fault is activated whenever the internal temperature exceeds 70 °C.
NORMAL
Top: temperature · Bottom: fault flag
Motor temperature settles at 50.72 °C against a 30 °C (303.1 K) ambient.
FAULT
Top: temperature · Bottom: fault flag
Trapped heat drives the temperature to 120.1 °C, above the limit; the fault flag is set.
Notes: Temperature rise and the fault indicator.

## Slide 22: Simulation Output: Normal vs Fault
NORMAL
FAULT
Parameter | Normal | Fault | Fault condition
Current | 0.5068 A | 1.357 A | > 0.9 A
Voltage | 24 V | 30 V | > 24 V
Vibration | 0.5147 | 3.459 | > 2
Temperature | 50.72 °C | 120.1 °C | > 70 °C
Notes: Lamps turn from green to red and status displays change from NORMAL to FAULT when each parameter crosses its limit.

## Slide 23: Simulation vs Hardware
Parameter | Simulation (MATLAB/Simulink) | Hardware (ESP32 prototype)
Supply | 24 V DC source | 24 V SMPS
Current | Fault > 0.9 A | ACS712-30A on GPIO34 · F01 > 8 A
Voltage | Fault > 24 V (30 V injected) | Divider sensor on GPIO35 · F02 < 20 V, F03 > 28 V
Temperature | Fault > 70 °C (thermal model) | DS18B20 on GPIO4 · F04 > 60 °C
Vibration | Fault > 2 (filtered ripple) | MPU6050 · F05 axis > 15 / 15 / 20 m/s²
Status output | Lamps and displays | OLED (12 pages) and Blynk (50 virtual pins)
Thresholds are set separately for the simulated motor and the hardware prototype.
Notes: The simulated monitoring logic is carried over to the ESP32 prototype with thresholds set for the hardware sensors.

## Slide 24: System Architecture
Interface
OLED Display
12 pages
Wi-Fi
Blynk Cloud
Mobile / Web
App
Processing
(ESP32)
Acquire
sensors
Power &
Energy
Fault
Detection
Motor
Protection
Health
Analytics
Flash
Logging
Sensing
Voltage Sensor
ACS712 30A
DS18B20
MPU6050
Power & Drive
24V SMPS
BLDC Driver
BLDC Motor
Sensor data flows up to the ESP32; the EN signal flows down to the driver.
Notes: Four layers: power and drive at the bottom, sensing above it, the ESP32 firmware in the middle, and the OLED plus Blynk cloud interface on top. Sensor data flows up; EN and PWM control flows down to the driver.

## Slide 25: Block Diagram
Power
Sensing
Data
Control
24V SMPS
DC supply
BLDC Driver
Motor drive
BLDC Motor
Machine under test
Voltage Sensor
across supply
ACS712
in series (current)
DS18B20
on motor body
MPU6050
on motor frame
OLED Display
SSD1327 · SPI
ESP32
Sense · Analyse · Protect
Wi-Fi → Blynk
Web / mobile dashboard
EN
Notes: Power path on top; sensors measure the motor and supply; the ESP32 processes and sends data to the OLED and Blynk.

## Slide 26: Hardware & Software Components
ESP32
Controller + Wi-Fi
BLDC Motor
Machine under test
BLDC Driver
Enable (EN) input
ACS712 30A
Current sensing
Voltage Sensor
Divider module, ×7.3
DS18B20
Temperature, 1-Wire
MPU6050
Accel + gyro, I2C
SSD1327 OLED
128×128 SPI display
24V SMPS
DC power supply
Software: Arduino IDE · ESP32 core · Blynk · U8g2 · Adafruit MPU6050 · DallasTemperature + OneWire · Preferences
Notes: Nine hardware parts and the role of each.

## Slide 27: Circuit Diagram: Power & Sensing
+24V
GND
24V
SMPS
ACS712 30A
IP+
IP−
5V supply
OUT → GPIO34 (ADC)
BLDC
Driver
VIN
GND
EN ← GPIO25 · PWM (fixed) ← GPIO26
U
U
V
V
W
W
BLDC
Motor
Voltage Sensor
VIN+ / VIN− across supply
S → GPIO35 (ADC)
+24V
GND
Motor phases
Signal
Tie ESP32 GND to SMPS GND (common ground).
Notes: 24V SMPS feeds the BLDC driver through the ACS712 (current sensed in series). The voltage sensor is connected across the supply. Motor phases U, V, W go to the motor. ESP32 ground is common with the supply ground.

## Slide 28: Circuit Diagram: Sensor Connections
ESP32 DevKit
GPIO34 (ADC)
GPIO35 (ADC)
GPIO4 (1-Wire)
GPIO21 (SDA)
GPIO22 (SCL)
VIN 5V → ACS712 VCC
3V3 → DS18B20 / MPU6050
GND → all grounds
ACS712 30A
OUT
5V
GND
Voltage Sensor
S
24V
GND
DS18B20
DATA
3V3
GND
VCC
GND
MPU6050
SDA
SCL
3V3
GND
VCC
GND
4.7k
3V3
ACS712-30A idles at 2.5 V and adds 66 mV per amp, so its output stays below 3.3 V up to about 12 A.
MPU6050: ±8 g, ±500 °/s, 21 Hz filter. Voltage module is scaled so 24 V ≈ 3.3 V (×7.3).
Notes: ACS712 OUT goes to GPIO34 and the voltage sensor output to GPIO35 (both ADC1). The DS18B20 data line uses GPIO4 with a 4.7k pull-up. The MPU6050 is on I2C: SDA GPIO21, SCL GPIO22.

## Slide 29: Circuit Diagram: OLED & Driver Control
ESP32 DevKit
GPIO25 (EN)
GPIO26 (PWM)
GPIO5 (CS)
GPIO27 (DC)
GPIO14 (RST)
GPIO18 (SCK)
GPIO23 (MOSI)
3V3 → OLED VCC
GND → driver and OLED GND
BLDC Driver
EN
PWM
GND
SSD1327 OLED
CS
DC
RST
SCK
MOSI
3V3
GND
VCC
GND
EN = HIGH runs the drive; the ESP32 pulls it LOW on over-current, over-voltage or over-temperature. PWM on GPIO26 is held at 100% duty, so speed is not controlled.
128×128 OLED on 4-wire hardware SPI, 3.3 V.
Notes: The SSD1327 OLED uses 4-wire hardware SPI: CS GPIO5, DC GPIO27, RST GPIO14, SCK GPIO18, MOSI GPIO23. The driver enable pin is GPIO25 and PWM is GPIO26.

## Slide 30: Working Principle & Flowchart
1
Initialize & Self-Test
2
Calibrate ACS712
3
Read Sensors
4
Power & Energy
5
Detect Faults
6
Protect & Health Analysis
7
Update OLED & Blynk
8
Repeat (500 ms)
Calibration runs once at start-up; step 8 returns to step 3. Blynk data is sent every 1 s.
Notes: Walk through the loop: initialise, read, calculate, detect, analyse, display, upload, repeat.

## Slide 31: Sensor Details
Sensor | Pin | Measures | Configuration | Used for
Voltage sensor | GPIO35 | Supply voltage | Divider module, reading × 7.3 | Under / over voltage
ACS712-30A | GPIO34 | Motor current | 66 mV/A, zero offset calibrated at start-up | Over current, stall, no load
DS18B20 | GPIO4 | Temperature | 1-Wire, −55 °C to +125 °C | Over temp, rapid rise, cooling health
MPU6050 | I2C 21 / 22 | Vibration | ±8 g, ±500 °/s, 21 Hz filter | High vibration, shock, bearing health
Calculations: P = V × I · E = E + P·Δt · Vibration = √(ax²+ay²+az²) · Load = I ÷ 10 A × 100 %
Notes: Each sensor, its ESP32 pin, how it is configured in the code, and which faults it feeds.

## Slide 32: Fault Detection
F01
Over Current
> 8 A
F02
Under Voltage
< 20 V
F03
Over Voltage
> 28 V
F04
Over Temperature
> 60 °C
F05
High Vibration
axis > 15 / 15 / 20 m/s²
F07
No Load
< 0.2 A for 5 s
F08
Motor Stall
> 6 A, low motion
F09
Sensor Failure
invalid or missing sensor
F10
Power Overload
> 180 W
F11
Current Fluctuation
step > 2 A
F12
Rapid Temp Rise
> 5 °C in 30 s
F13
Shock
axis > 25 / 25 / 30 m/s²
F14
High Energy
> 1000 Wh
F15
Blynk Offline
cloud disconnected
Notes: Fourteen fault codes. They are checked in priority order and the first match is reported as the motor status.

## Slide 33: Motor Protection & Control
Fault flags
Over current, over voltage or over temperature.
ESP32 logic
Checked on every loop cycle, about 500 ms.
Enable pin
GPIO25 is driven LOW to disable the driver.
Motor stops
Drive stays off until the fault clears.
Automatic restart
EN returns HIGH as soon as all three fault flags clear.
Fixed drive level
GPIO26 outputs 10 kHz PWM held at 100 % duty; the motor speed is not controlled.
Notes: When over-current, over-voltage or over-temperature is detected, GPIO25 (EN) goes LOW and the driver is disabled. It re-enables automatically when the faults clear.

## Slide 34: Predictive Maintenance
Health Score
100 − penalties
Below 60 → service required
≥ 90
EXCELLENT
≥ 75
GOOD
≥ 60
WARNING
≥ 40
SERVICE
< 40
CRITICAL
Bearing
Vibration above 18 and 25 m/s²
Cooling
Temperature above 45, 55 and 65 °C
Electrical
Current above 5 / 7 A, voltage below 22 V or above 26 V
MOTOR HEALTH
Average of the three, giving remaining life and wear %
Output: CHECK BEARING · CHECK COOLING · CHECK POWER · GENERAL SERVICE · NORMAL
Notes: Health score from temperature, current, voltage and vibration; sub-health values for bearing, cooling and electrical; the average gives motor health, remaining life and wear.

## Slide 35: Performance & Diagnostics
Statistics
Maximum and average of voltage, current, temperature, power and vibration.
Performance analysis
Estimated efficiency and power factor, load %, performance and reliability index.
Self-diagnostics
Six checks: voltage, current, temperature, MPU6050, Wi-Fi and Blynk.
Data logging
Energy, run time and fault count saved every 30 s; last 10 faults kept with time.
Notes: Beyond fault detection the firmware tracks statistics, estimates performance, self-checks six items and stores key data in flash.

## Slide 36: OLED Output (12 Pages)
1
Institution
Title page
2
Drive System
V · I · P · E
3
Temperature
Value and state
4
Vibration
AX · AY · AZ
5
System
Motor, I, V, vibration
6
Fault Status
Code · event · count
7
Motor Health
Score · run time
8
Fault History
Last 5 faults
9
Statistics
Max / average values
10
Predictive
Bearing · cooling · life
11
System Status
Sensors, Wi-Fi, Blynk
12
Performance
Eff · load · PF
Pages rotate automatically every 3 seconds on the SSD1327 display.
Notes: The 128×128 OLED rotates through twelve pages, changing every three seconds.

## Slide 37: Blynk Dashboard
Blynk Console: BLDC Motor Monitor dashboard with gauges for voltage, current, temperature, power, energy, health score, performance status and load.
Datastream groups
Live data
V0–V4, V9
Fault & status
V5–V8, V16–V18
Vibration
V10–V15
Statistics
V19–V26
Predictive health
V27–V33
Diagnostics
V34–V41
Performance
V42–V49
Notes: Insert your dashboard screenshot. The right side lists the data stream groups sent every second (V0–V49).

## Slide 38: Experimental Setup
IN THE PHOTO
ESP32 and sensors
BLDC driver and motor
24 V SMPS
1.5-inch OLED
Prototype: ESP32 with ACS712, voltage sensor, DS18B20 and MPU6050, powered from a 24 V SMPS through a BLDC driver.
Notes: Photo of the working prototype: ESP32 on a breadboard, 24 V SMPS, BLDC driver and motor, and the 1.5-inch OLED module.

## Slide 39: Expected Outcomes
Intelligent, self-monitoring BLDC motor drive implemented
Automatic protection on over-current, over-voltage and over-temperature
Real-time monitoring of current, voltage, temperature and vibration
Energy consumption analysis and efficiency monitoring
Early fault detection using multi-parameter condition monitoring
Predictive maintenance alerts to reduce unexpected breakdowns
IoT remote monitoring through an ESP32 dashboard
Validation through MATLAB/Simulink and a hardware prototype
Improved reliability, less downtime and lower maintenance cost
Low-cost smart motor drive for industrial automation
Notes: Ten outcomes the project set out to achieve.

## Slide 40: Future Scope
AI fault prediction
Learn from fault history to forecast failures.
SCADA integration
Connect to plant-level supervisory systems.
Cloud analytics
Long-term trends and multi-motor analysis.
RPM / Torque sensing
Add speed and torque for deeper diagnosis.
Notes: Four directions to extend the project.

## Slide 41: Conclusion
A low-cost ESP32-based intelligent BLDC drive that monitors voltage, current, temperature and vibration, detects faults, protects the motor and predicts maintenance, validated through MATLAB/Simulink simulation and a hardware prototype.
Real-time monitoring
Fault detection
Predictive maintenance
Notes: Summarise what was achieved.

## Slide 42: References
1
Raja, H. A., Raval, H., Vaimann, T., Kallaste, A., Rassolkin, A., & Belahcen, A. (2022). Cost-efficient real-time condition monitoring and fault diagnostics system for BLDC motor using IoT and machine learning.
2
IoT based condition monitoring and control of induction motor using Raspberry Pi (2022).
3
do Nascimento, L. S., da Silva, E. P., & Pereira, E. G. (2024). Development of a data acquisition and monitoring system for electric motors using the Internet of Things. CBA 2024. doi:10.20906/CBA2024/4526
4
Arman Sabri, A. S., & Aziz, R. (2025). Motor vibration and temperature detector by using IoT. Evolution in Electrical and Electronic Engineering, 6(2), 347–355.
5
Wan Mohd Supian, W. R., Mohd Nordin, I. N. A., Khamis, N., & Muhammad Razif, M. R. (2022). Electrical machine breakdown monitoring system using IoT. Journal of Advanced Industrial Technology and Application, 3(2), 1–7.
6
ESP32, Arduino and Blynk IoT documentation.
7
Datasheets: ACS712, DS18B20, MPU6050 and SSD1327.
Notes: Full citations for the reviewed papers.

## Slide 43: Thank You